Bidimensional Lattice Boltzmann Implementation using CUDA
Antonio Lucas N. de O. Barros
Cátia Souza do Nascimento
João Lima
CMP 557 - 2010/1
Programming Massively Parallel Processors using CUDA
Instituto de Informática
PPGC - UFRGS

---
Outline
- Lattice Boltzmann
- Implementation
- Experimental Results
- Conclusion
- Future Work

---
Lattice Boltzmann
- Iterative Numeric Method
- Mesoscopic
- Relation with LGA method
  - Particle Representation:
    - MLB Uses real distribuitions
    - LGA uses boolean distributions

---
Lattice Boltzmann
- Lattice Structures
  - D2Q9 – 2 Dimensions, 9 directions
  - D3Q19- 3 Dimensions,19 directions
D2Q9
D3Q19

---
Implementation
- D2Q9 – 2 Dimensions, 9 directions
- Based on: Schepke and Maillard (2009) sequential implementation

---
Implementation
- C++ code + CUDA kernels (4)
- Each direction is a thrust vector
  - thus, 9 thrust vectors
- Between kernel calls, data remains in GPU memory
  - CPU-GPU copies before/after the iteractions

---
Implementation
LBM(lb, input, output)
1 lb ← read obstacles from input
2 lb ← read parameters from input
3 for i ← 0 to lb.Maximum_iteractions() do
4	lb.Redistribute_kernel()
5	lb.Propagate_kernel()
6	lb.Bounceback_kernel()
7	lb.Relaxation_kernel()
8 lb.Write_Results( output )

---
Implementation - Redistribute
- Calculate the macroscopic density and speed from the values of each lattice point
- Partitioning by y axis
  - each thread process a line

---
Implementation - Propagate
- Propagate the particles distribution to all neighboring cells
- Blocked partitioning by x and y axis

---
Implementation - Bounceback
- Represents Boundary Conditions
- Invert the speed vector direction when collisions occur
- Blocked partitioning by x and y axis

---
Implementation - Relaxation
- Use the equilibrium value to apply in the distribution function of each lattice point
- Blocked partitioning by x and y axis

---
Experimental Results
- Hardware Used:
  - Core i7 @ 2.80 Ghz / GTX480 (Fermi)
- Graphics with execution time and speedup
- Three different inputs
  - lattice of 30x20
  - lattice of 200x50
  - lattice of 512x512

---
Experimental Results
The obstacle in our 2D tests, and 3D example

---
Experimental Results
Output example (512x512 with 90 iteractions)

---
Experimental Results
LBM - Execution Time Core i7/GTX 480 (Fermi)
input size
time (s)

---
Experimental Results
LBM - Speedup Core i7/GTX 480 (Fermi)
input size
speedup

---
Conclusion
- Lattice Boltzmann can be efficient in GPUs
- Different result values (error )
  - the precision of GPU was float, CPU double
- Coding in CUDA is difficult with many variables
  - in our case, dimensions
10^{-4}

---
Future Work
- Optimize kernel functions
  - memory accesses
  - arguments
  - etc
- Use Fermi shared memory
- D3 version (D3Q15 or D3Q19)

---
References
Schepke and Maillard (2009). Parallel Lattice Boltzmann Method with Blocked Partitioning. International Journal of Parallel Programming, 2009, 37, 593-611.

---
Bidimensional Lattice Boltzmann Implementation using CUDA
Antonio Lucas N. de O. Barros
Cátia Souza do Nascimento
João Lima
CMP 557 - 2010/1
Programming Massively Parallel Processors using CUDA
Instituto de Informática
PPGC - UFRGS